## Slide 1: Submerged Arc Welding ANSYS APDL analysis
Modal analysis of Mild Steel plates before and after SAW

## Slide 2
ANSYS APDL main screen
Main Menu
Geometry Display
Command Line

## Slide 3
Select Element type
1
SHELL 181
4 noded element

## Slide 4
Add Material Property
2
Ex =2.1e11
PRxy = 0.3
DENS = 7850

## Slide 5
Add Plate Cross-Section
3
Thickness = 0.01 m

## Slide 6
Copy Area, Keypoint inter-connectivity data
And
Paste in APDL Command Line and press ENTER
Copy Co-ordinate data
And
Paste in APDL Command Line and press ENTER
Keypoints – 88
Area – 141
Geometric Modelling (Keypoints and Area)
4
Commands –
/PREP7 – initialize Model creation preprocessor
K,n,x,y,z – Create Keypoint number ‘n’ at ‘x’, ‘y’, ‘z’ coordinate
A,1,2,3 – Create a triangular area between Keypoints 1,2,3

## Slide 7
1
2
Meshing
5

## Slide 8
Analysis Type
6
Modal Analysis
Free-Free Boundary condition
Modes to be extracted – 15
(including 6 Rigid modes)

## Slide 9
Solve for Solution
7

## Slide 10
Results (Post Processing)
8
Detailed Summary in List Results

## Slide 11: Compare Results Before and After SAW
Deformation in plate due to thermal expansion and residual stresses generated during SAW.
Change coordinate data measured after welding and repeat all the steps(1-8).
Notice change in natural frequency of plate before and after SAW.

## Slide 12
Results (Before and After)
Before SAW
After SAW